# Text boxes

- Ensure that the substrate is clean, dry and free from contaminants.

- Using a trammel or similar, mark the radius required onto the subfloor.

- Following the line marked on the floor, run a bead of mastic cartridge adhesive along the line for approximately 600mm – 800mm.

- Working from the end, place the base into the adhesive and begin to mechanically fix the base to the floor through the tabs. (No.6 screw).

- Once the base has been installed and the adhesive has fully dried, the floor on either side of the profile can be prepared to accept the floorcovering to be installed.

If any further information is required, please do not hesitate to contact Gradus Technical Services on (+44)1625 428922 or fax on (+44)1625 425226

Data Sheet:   (sheet 1 of 1)   22/04/10

# Accessories

Installation Guidelines

Gradus Accessories, Park Green, Macclesfield, Cheshire SK11 7LZ England UK  Tel: 01625 428922  Fax: 01625 433949

www.gradusworld.com

GT61R