For Ceramic Installations

- Choose the trim height according to the thickness of the tile.  The trim should not exceed the height of the tile but should be 0.5 to 1mm lower.

- It should be ensured that all surfaces to which the profile is to be fixed are dry, flat and free from any contaminants.

- Cut the profile to the size required and allow space for linear expansion.

- Apply adhesive to the area and bed the perforated flange of the profile into the adhesive and align.

- Trowel extra adhesive over the perforations and the dovetail groove in the vertical section.

- Bed the tile into the adhesive and align with the profile leaving a gap of between 0.5 to 2mm for final grouting to be undertaken.

For other floor coverings

- It should be ensured that all surfaces to which the profile is to be fixed are dry, flat and free from any contaminants.

- Cut the profile to the size required.

- Apply a bead of proprietary cartridge adhesive to the undersides of the profile and firmly place into position.

Note:

This profile is designed for use with a liquid penetrant (such as with ceramic tiles or resin floors where the liquid or adhesive under the ceramics sets to a stiff solid) and therefore doesn’t warrant the need for a mechanical fix with screws.

Although there are holes in these products, these are to allow liquid or adhesive to flow through them and form an additional mechanical bond. If the depth allows for the use additional screws can be used but are not essential. Guidance for which follows on from step 2:

- Place the profile into position and through the pre-drilled holes, mark the substrate.

- Drill the marked substrate using a 6mm drill bit and once drilled insert the appropriate sized plug (6mm = red plug).

- Apply a bead of proprietary cartridge adhesive to the underside of the profile, then, ensuring the substrate is free from dust, firmly place the base into position.  *On timber subfloors, apply adhesive, and fix using No6 wood screws.

- Secure in place using a No6 fixing screw.

If any further information is required, please do not hesitate to contact Gradus Technical Services on (+44)1625 428 922 or

fax on (+44)1625 433 949.