# Text boxes

# Safety & Protection Systems

Installation Guidelines

Data Sheet:   (sheet 1 of 1)   September 2015

Flexi-Posts

REQUIREMENTS

| SETTING OUT | POWER TOOLS | HAND TOOLS | DRILLS / BITS / ATTACHMENTS | FIXINGS |
| --- | --- | --- | --- | --- |
| Marker Pen Tape Measure | SDS Drill 110V Impact Wrench 110V | Spanner/Ring Spanner 17mm AF | 12mm SDS M10 Socket 17mm AF | Typical fixings used are M10 Coach Screw and Plug (3 no. included with post) |

FLEXI PROTECTION POST (HEIGHT OPTIONS)

- FDP-800-Y	Flexi-Post 800mm High

- FDP-1000-Y	Flexi-Post 1000mm High

Fixings included
Site specific fixings may be required – consult with your project team and or call the Gradus technical team to discuss options

SUITABLE SUBSTRATES

- Concrete – Slab Grade/Thickness => C25 / =<100mm

- Tarmac =>100mm Thick

PLACEMENT / SETTING OUT

- Typical positioning will be a minimum of 100mm from wall/corner/reveal to edge of baseplate.

- Ensure the post is typically 25mm past the line of traffic / wall to ensure adequate protection from traffic flow

- Place post, mark fixing holes and set aside no.

DRILLING & FIXING

- Using SDS 110 volt Drill rig – drill to approx. 125mm deep

- Ensure all debris is cleared from hole

- Clean out holes with blow pump and ensure drilling is vertical in both planes to give a nice flush fixing

- Place post, insert M10 coach screws as appropriate

- Tighten with Impact Wrench 110v and or Spanner

FINISHING

- Clean-down

Gradus Accessories, Park Green, Macclesfield, Cheshire SK11 7LZ England UK  Tel: 01625 428922  Fax: 01625 433949

www.gradusworld.com